Operating system -                    2-axis 4-beam pulse Doppler sonar or

ROT-combined 3-axis 4-beam pulse Doppler sonar (ROT: option)

Operating frequencies -           240 kHz (BT: for speed against the ground)

2MHz (WT: for speed against the water)

Speed range-                               BT Fore/Aft: -10.00 to +40.00 kts

Port/Stb.: -9.99 to +9.99 kts

Stern P/S: -9.99 to +9.99 kts (with optional ROT)

WT Fore/Aft: -10.00 to +40.00 kts

Distance run range-                   0 to 99999.99nm

Depth range-                               BT: 2 to 250m (below hull bottom) depending upon sea bottom conditions

WT: 3m or more (below hull bottom)

Speed measuring accuracy-    ±1% or ±0.1 kts whichever is greater

Total distance run accuracy-  ±1% or ±0.1 nm whichever is greater

Ship speed indication-              XX.XX 4-digit indicator (in kts or m/s) (P/S: 3-digit) Analog indication (in kts)

IEC61162-1 inputs-                   ROT (Stern P/S speed) **ROT (excl. GPROT)

(NMEA0183)                             GPS (GPS ship speed) GGA, RMC, RMA, GLL, VTG

GYRO (GPS ship speed) HDT, HDG

Data outputs-                             IEC611621:2000 outputs: 5 circuits VBW, VLW, DPT, DBT

DC voltage output: 2 circuits (for analog indicator)

Opto coupler signal: 8 circuits (200 pulses/nm)

Relay closure signal: 1 circuit (200 pulses/nm)

Relay closure signal: 1 circuit (Power fail alarm)

Power supply-                            100/110/115/220/230VAC

±10%, 50/60Hz, single-phase

Power consumption-                 300 VA or less

Operating temperature-            -15 to +55℃