SAILOR 6282 AIS Transponder

Weight -  1.15 kg

Dimensions -  (L x W x H) 160 x 270 x 42 mm

Equipment class - Protected, according to IEC 60945

Input voltage - 10.8VDC to 31.2VDC

Power consumption - 12W (0.5A @24 VDC input voltage)

Temperature: -15°C to +55°C (Operational)

-30°C to +80°C (Storage)

Compass Safe Distance - 55 cm (standard magnetic compass)

- 45 cm (Emergency magnetic compass)

Receivers - 156.025 - 162.025 MHz (TDMA)

- 156.525 MHz (Channel 70, DSC)

Channel bandwidth -  25 kHz

RF Output Power - High: 12.5 W

- Low: 1W

- Low power forced control (gas alarm): 1W

Frequency - 156.025 - 162.025 MHz

VHF connector - TNC female

GPS connector - TNC female

VHF and GPS cable - RG214 or better

Connection to SAILOR 6004 Control Panel - LAN (LWE IEC 61162-450)

Connections to sensors and PI - 50 pin sub-D

SAILOR 6285 GPS Antenna - Active

Dimensions - Ø: 91 mm, H: 77.5 mm

Weight - 0.15 kg

Mounting - Bracket mount on pipe, thread 1” x 14 TPI

Equipment class - Exposed, according to IEC 60945

Antenna type - Active patch antenna

Frequency - 1570 to 1608 MHz

Impedance - Nominal 50 Ohm

Polarization - Circular right-hand

Coverage - Hemispherical

Selectivity - 45 dB down at center ±25 MHz

Gain - 28 dB

Supply voltage - 5 ±1 VDC

Current consumption - Approx. 30mA

Connector-  TNC female

Cable - RG214 recommended

Operating temperature: -40°C to +55°C

Storage temperature: -40°C to +80°C

SAILOR 6283 AIS Connection Box and Wall Tray

Weight without SAILOR 6282 AIS Transponder - 2.15 kg

Weight with SAILOR 6282 AIS Transponder mounted- 3.30 kg

Dimensions - (L x W x H) 340 x 310 x 55 mm

Equipment class - Protected, according to IEC 60945

SAILOR 6004 Control Panel

Mounting method - Flush mount or bracket

Voltage - 10.8 to 31.2 V DC

Power consumption - Typical: 18 W active

- Peak: 42 W

- 3.15 A internal fuse (non-serviceable)

Audio output - Up to 6 W in 8 Ohm

Interfaces - 2 x Ethernet (10/100 Mbit/s), Accessories connector, Auxiliary connector

Compliance - IEC 60945, IEC 60950-1

IP rating - IP54

Ambient temperature: -15°C to 55°C

Storage temperature: -30°C to 80°C

Compass safe distance - 0.6 m

Dimensions - W x H x D 191 mm x 145 mm x 61 mm (without mounting bracket)

Weight - 1.1 kg (1.25 kg with mounting bracket)

ThraneLINK

ThraneLINK is a sophisticated communication protocol that connects the SAILOR products in a network, offering important new opportunities to vessels. It provides facility for remote diagnostics and enables access to all the SAILOR products from a single point for service. This results in optimized maintenance and lower cost of ownership because less time is needed for troubleshooting and service. Installation is made easier as ThraneLINK automatically identifies new products in the system. The uniform protocol is an open standard which provides a future proof solution for all vessels