JHS-183

IMO type approved	✓

Frequency	156.025-162.025 MHz, default channels 161.975 MHz, 162.025 MHz, DSC (receive only): 156.525 MHz

Frequency accuracy	Within ±3 × 10-6

Channel spacing	25 kHz

Type of emission	AIS: G1D (F1D)

Type of modulation	AIS: GMSK

Power	19-35V DC (optional power supply 100-220V AC)

Consumption	Up to 3.0A (transmitting), up to 1.0A (receiving)

Output power	12.5W/1W

Display

New

4.5-inch FSTN LCD (128 by 64 pixels)

Keyboard	12 (backlit) keys

Dimmer	4 levels

Interfacing (standard)	IEC61162-1/2 input: 2 ports (GPS, gyro) IEC61162-2 in/output: 1 port (radar or ecdis)

Interfacing (with connection box)	IEC61162-1/2 input: 3 ports (GPS, gyro, speed log)

IEC61162-1/ITU-R M, 823-2: 1 port (DGPS)

IEC61162-2 in/output: 3 ports (radar, ecdis, long range)

IEC61993-2 alarm output: 1 port

IEC61162-1 input	GNS, GLL, DTM, GBS, VBW, RMC, HDT, ROT, GGA, VTG

IEC61162-2 input	ABM, ACA, ACK, AIR, BBM, LRI, LRF, VSD, SSD, EPV, HBT, VDS, AIQ

IEC61162-2 output	ABK, ACA, ALR, DSC, DSR, LRF, LR1, LR2, LR3, TXT, VDO, VDM, TRL, VER, NAK

LAN

New

IEC 61162-450: 1 port (for maintenance and ship's network)

Pilot plug	IEC61162-2 in/output: 1 port

Pilot plug input	ABM, ACA, ACK, AIR, BBM, EPV, SPW, HBT, SSD, VSD, AIQ

Pilot plug output	ABK, ACA, ACS, ALR, TRL, TXT, SSD, VSD, VDM, VDO, VER, NAK, DSC, DSR

Transponder connection	Single coax cable (up to 50 m) from display to transponder

Ambient conditions	Operating temperature: -25° to 55°C (transponder) -15° to 55°C (display, connection box)

IP protection rate: IP56 (transponder), IP55 (display)

Relative humidity: 0% to 95% non-condensing